## Slide 1: Reinforcement Learning Applied to Autonomous Vehicles
GUYOT Antonin

## Slide 2: Content
Context
  QCAR presentation
  Reinforcement Learning introduction
Strategy and results
  Bicycle model control
  Simulation with MATLAB/Simulink
  HiL integration
Conclusion

## Slide 3: QCAR presentation
Developped by Quanser
MATLAB Toolbox
Control with WiFi
LIDAR, 360 Vision, RGBD Camera, Accelerometers

## Slide 4: Reinforcement Learning (RL) introduction
RL => an agent tries to learn a policy by trial and error
Setup :
  Observations
  Actions
  Reward
DDPG => Policy Iteration (actor/critic architecture)
  Actor applies the policy
  Critic looks at the associated reward to tune the policy
Notes: Policy Iteration => Learn a policy that maximises the reward with observations in a continuous state
Actor critic architecture =>

## Slide 5: Reinforcement Learning (RL) introduction
Actor-critic network
Q-value
  Train actor : Maximize Q
  Train critic : Minimize Q – (reward + γ Qnext)
Replay Buffer
Critic
Actor
obsnext
actnext
Critic
act
obs
Q
Qnext
Notes: Gamma : discount (0,99) => long term reward
Use of a target network to freeze the critic while training the actor, and freeze the actor and next critic while training the critic
Train actor => inject observation and try to maximise Q
Train critic => inject observation, action and next observation and try to minimize

## Slide 6
Reference
Observations
Controller
Policy
Plant
Environment
RL Algorithm
Policy
update
Measurements
Measurements
State feedback
Control
input
Actions
Traditional control
RL
Notes: Gamma : discount (0,99) => long term reward
Use of a target network to freeze the critic while training the actor, and freeze the actor and next critic while training the critic
Train actor => inject observation and try to maximise Q
Train critic => inject observation, action and next observation and try to minimize

## Slide 7
Actor
observation
action
Critic
observation
Q
action
Notes: Gamma : discount (0,99) => long term reward
Use of a target network to freeze the critic while training the actor, and freeze the actor and next critic while training the critic
Train actor => inject observation and try to maximise Q
Train critic => inject observation, action and next observation and try to minimize

## Slide 8
Actor
obsnext
actnext
Critic
Qnext
act
Critic
Q
obs
Notes: Gamma : discount (0,99) => long term reward
Use of a target network to freeze the critic while training the actor, and freeze the actor and next critic while training the critic
Train actor => inject observation and try to maximise Q
Train critic => inject observation, action and next observation and try to minimize

## Slide 9: Bicycle model control
Simplified representation of a 4 wheels vehicle
2 wheels, one steering wheel
Represented by a position and an orientation, controled by a velocity and a steering angle

## Slide 10: Bicycle model control
To get started => work of Peter Corke
Point to point control
  Goal of coordinates

## Slide 11: Bicycle model control
Simulink Model
Notes: Had to update it => TP preparation

## Slide 12: Simulation with MATLAB Simulink
Modelisation of the components
  Environment
  LIDAR

## Slide 13: Simulation with MATLAB Simulink
RL Toolbox

## Slide 14: Simulation with MATLAB Simulink
First experiment : move freely in a space with obstacles while avoiding them
Observations
Actions
  Velocity control
  Steering control
Reward
Take a measurement
Collision ?
Reward = -10
Near the wall ?
Reward = distance to wall
Reward = distance to wall + speed
Yes
Yes
No
No

## Slide 15: Simulation with MATLAB Simulink – Obstacle
Help convergence : MinMax normalization

## Slide 16: Simulation with MATLAB Simulink – Obstacle
First result : no good policy

## Slide 17: Simulation with MATLAB Simulink – Obstacle
Second result : convergence

## Slide 18: Simulation with MATLAB Simulink – Obstacle
Improvements
  Let it train for longer
  Improve reward function
  Better control of velocity (backtracking)

## Slide 19: Simulation with MATLAB Simulink
Second experiment : Point to point drive
Observations
  Distance and orientation from goal
  Relative position from goal
Actions
Reward
Measure relative position
Aligned in one axis ?
Reward = 0
Arrived to goal ?
Reward = 5
Reward = 2
Yes
No
No
Yes

## Slide 20: Simulation with MATLAB Simulink – Point to Point
Simplified environment

## Slide 21: Simulation with MATLAB Simulink – Point to Point
Results : no good policy

## Slide 22: HiL integration
Use of Quanser Toolbox
Velocity and steering control

## Slide 23: HiL integration
LIDAR informations acquisition

## Slide 24: HiL integration
Calculations made on bicycle model and control injected to the QCAR
Notes: Calculation AND supervision of the system

## Slide 25: Conclusion
Discovery of RL algorithms
  Correlation between simulation and reality
  Results analysis
  Difficulty => DDPG complete understanding (black box)
  Next step => fully integrate HiL and try more difficult tasks
Appropriation of a simplified but complex model
Hang of the QCAR and embedded system (and problems associated)
Notes: J’ai pris en main => I got the hang of

## Slide 26: Thank you for listening ! Any questions ?